## Slide 1: First Results of DOSUE-RR Search for dark photon CDM in the mass range
Osamu TAJIMA (Kyoto U.)
On behalf of the DOSUE-RR collaboration
https://arxiv.org/abs/2205.03679

## Slide 2: What’s DP-CDM?
Dark-photon
D. Horns et al. , JCAP 1304, 016 (2013)
Boundary condition at the surface,
EM-fields of DP-CDM appear via Kinetic mixing
DP-CDM
Almost perpendicularly emitted from the boundary
“Conversion photon”
Metal plate
(Boundary of EM field)
Cold Dark Matter

## Slide 3: Detection principle of DP-CDM
N. Tomita, S. Oguri, et al. , JCAP 09, 012 (2020)
converter
Metal plate
(boundary of EM)
millimeter-wave
Radio receiver
Horn antenna
DP-CDM
Spectrometer
Conversion
photon (perpendicular within 0.1˚)
D. Horns et al. , JCAP 1304, 016 (2013)
Power (W)
Peak height
Peak freq.  mass
e.g.,
Simulated spectrum of conversion photon
~ ~

## Slide 4: Constraints to date
CMB etc.
Solar lifetime
Axion
Haloscope
Dish antenna
Tomita et al.

## Slide 5: Constraints to date
* Motivations from string theories and inflation models, e.g., JCAP 1304, 016 (2013), Phys. Rev. D 93, 103520 (2016).
CMB etc.
Solar lifetime
Axion
Haloscope
Dish antenna
Tomita et al.
No strong constraint here*
DOSUE-RR is series of experiments
to explore wide region!

## Slide 6: The DOSUE-RR Collaboration
Kyoto University
University of Tsukuba
Shunsuke Honda Recently moved from Instituto de Astrofisica de Canarias (IAC)
Dark-photon/dark-matter Observing System for Un-Explored Radio-Range
__ Do-Su-E.
(local phrase
in Kyoto)
Shunsuke Adachi
Ryo Fujinaka
Shumpei Kotaka
Hironobu Nakata
Yudai Seino
Yoshinori Sueno
Toshi Sumida
Junya Suzuki
Osamu Tajima
Soichiro Takeichi

## Slide 7: Major Noise?
Thermal radiation from ambient is major noise
Conversion photon is faint!
Under standard assumption - -
_____
for spectrum bin width of 2 kH
converter
Metal plate
(boundary of EM)
millimeter-wave
Radio receiver
Horn antenna
DP-CDM
Spectrometer
Conversion
photon (perpendicular within 0.1˚)

## Slide 8: Instrumental concepts
converter
Metal plate
(boundary of EM)
millimeter-wave
Radio receiver
Horn antenna
DP-CDM
Spectrometer
Conversion
photon (perpendicular within 0.1˚)
Maintenance the system and optical path in the cryogenic shield at ~3 K
Thermal radiation from ambient is major noise
Suppression of thermal noise
(same strategy as recent CMB experiments)

## Slide 9: Instruments
Aluminum plate
Window
Vacuum chamber
30 K shell
3 K shell
Horn antenna
GM refrigerator
1.7 m
0.4 m
Signal analyzer
ANRITSU MS2840A
Conversion photon
C-LNA (+30 dB) LNF-LNC15-29B
set in cold box
Bias electronics
W-LNA (+40 dB) Aldetec ALM-1826S210
Vacuum gauge monitor
Thermometer monitor
Success to achieve low system noise ( of ambient)

## Slide 10: Instruments cont.
Aluminum plate
Window
Vacuum chamber
30 K shell
3 K shell
Horn antenna
GM refrigerator
Conversion photon
C-LNA (+30 dB) LNF-LNC15-29B
set in cold box
My master
thesis research!

## Slide 11: Calibration: gain
millimeter-wave
Radio receiver
Horn antenna
Spectrometer
Maintained in the cryogenic condition
Blackbody source
Radio aborber
(ECOSORB CV3)
@ 77K & 290K
Typical gain
G = +62 dB
Typical time variation
< 1% in hour-scale
Raw signal is amplified by LNAs

## Slide 12: Calibration: Aeff
Effective aperture area is smaller than physical area because of finite beam resolution
Horn antenna
Beam width
Simulation at 20 GHz

## Slide 13: Data set for exploration
Swept power from 18 GHz – 26.5 GHz
  Freq. limit by waveguide cutoff, capability of SA
  FFT at RBW of 300 Hz (analysis bin width of 2 kHz)
  Bandwidth of single FFT scan is limited at 2.5 MHz
Frequency (GHz)
18.0
26.5
…
…
…
Gain calibration
Every 100 MHz interval
(~40 min)
Took 12 days to explore whole range
Nov. 29 – Dec. 10, 2021

## Slide 14: An example of spectrum data
Frequency (kHz + 18 GHz)
Power (x10-19 W)
stat. error
Expected sensitivity we achieved:

## Slide 15: Methodology of Signal Extraction
Power (W)
Fit function
Extract for each , i.e., sweeping fits
Signal power shape
Baseline offset
The Maxwell-Boltzmann
Simulated spectrum of conversion photon
~ ~
Isothermal perturbation

## Slide 16: Results of Signal Extraction
No significant excess at specific freq.
Taking into account “look-else-where” among all 4,250,000 fit results
Global p-value under null hypothesis: 68%
Found NO significant
signal
Null signal hypothesis

## Slide 17: Further investigation with more statistics
Stat.
Additional data in Jan. 17, 2022
Confirmed NO signal
No discovery??
Even though , we don’t wanna miss discovery
Confirmed zero-consistent results

## Slide 18: Systematic Errors
Source | Syst. error for
Gain | 4.0
Aeff | 4.2
⍴CDM | 3.9
Frequency resolution | 0.6
Alignment of instruments | < 0.1
Direction of conversion photon | < 0.1
Total | 7.0
Source | 
Gain | 4.0
Aeff | 4.2
⍴CDM | 3.9
Frequency resolution | 0.6
Alignment of instruments | < 0.1
Direction of conversion photon | < 0.1
Total | 7.0
Uncertainty of calibration
Model uncertainty

## Slide 19: Upper limits at 95% C.L.
The first exploration in
The most stringent constraint to date, and tighter than cosmological constraints
CMB etc.
Solar lifetime
Axion
Haloscope
Dish antenna
This work!

## Slide 20: First Results of DOSUE-RR
Searched for DP-CDM using cryogenic, i.e., low thermal noise, millimeter-wave system
Found NO significant signal
Set the most stringent limits to date Tighter than cosmological constraints
https://arxiv.org/abs/2205.03679
Summary
Dark photon/dark matter Observing System for Un-Explored Radio Range

## Slide 21: Stay Tuned!
This results
(K-band)
DOSUE-RR is
series of experiments
Systems for 8 – 18 GHz (J-band) & 170 – 260 GHz (Y-band) are in prep.

## Slide 22: Extra Slides

## Slide 24: “Null Samples”
Signal + Noise
Signal + Noise’
Noise only
Data set A
Data set B
Null sample (A-B)
We have 12 data samples
462 combinations for making null samples
Checking potential systematics
Optimizing analysis
Calculation of statistical significance
Entries

## Slide 25: Freq. bin-width for analysis
Raw data (interval 76.3 Hz) has correlations among neighbor bins because of the window function (RBW 300 Hz) is not perfect top-hat shape. This makes a bias for error estimation in the fits for signal extraction
Taking wider bin (i.e., re-binning) mitigates the effect of the correlation in the raw data
Optimized bin-width using ”null samples”
RBW 300 Hz
Correlations
Re-binning
Data samples for signal extraction

## Slide 26: Statistical analysis
The is obtained using the fit results for null samples
Entries
Given by the fraction above each fit result ()

## Slide 27: Statistical analysis
Consistency between the explored samples and null samples

## Slide 28: “dSpec”, DAQ speed x1000
RFSoC based spectrometer is underdevelopment
Wideband width ~2 GHz  DAQ speed x1000 comparing to the commercial signal analyzer

## Slide 29: What’s DP-CDM?
Dark-photon
D. Horns et al. , JCAP 1304, 016 (2013)
Boundary condition at the surface,
EM-fields of DP-CDM appear via Kinetic mixing
DP-CDM
Almost perpendicularly emitted from the boundary
“Conversion photon”
Metal plate
(Boundary of EM field)
Cold Dark Matter