## Slide 1: Updates on muon g-2/EDM experiment at J-PARC
June 20, 2018
Tsutomu Mibe (KEK)
www.g-2.kek.jp

## Slide 2: Summary
We plan to measure muon’s g-2 and EDM with ultra-cold muon beam at J-PARC.
  Complemental & independent from BNL and Fermilab g-2 measurements
News since last year
  Oct. 2017, First muon acceleration to 90 keV
  Mar 2018, Cross calibration of NMR probes (J-PARC,Fermilab)
  April 2018, Major funding for construction of the upstream muon beamline is provided.
  May 2018, Received very positive replies from the TDR review committee (FRC)
  (July 2018), Waiting for full approval from the lab.

## Slide 3
Production target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Silicon
Tracker
66 cm
Super Precision Storage Magnet
(3T, ~1ppm local precision)
Features:
Super-low emittance muon beam
No strong focusing
Compact storage ring
Full tracking detector
Completely different from BNL/FNAL method

## Slide 4: muon g-2 and EDM measurements
In uniform magnetic field, muon spin rotates ahead of momentum due to g-2 = 0
BNL E821 approach
γ=30 (P=3 GeV/c)
J-PARC approach
E = 0 at any γ
J-PARC E34
general form of spin precession vector:
FNAL E989

## Slide 5: Muon beam at BNL/FNAL
Conventional muon beam
proton
π+
μ+
pion
production
decay
emittance
~1000π mm・mrad
Strong focusing
Muon loss
BG π contamination

## Slide 6: Muon beam at J-PARC
Ultra-cold
muon beam
Conventional muon beam
proton
π+
μ+
pion
production
decay
cooling
μ+
emittance
~1000π mm・mrad
emittance
1π mm・mrad
Strong focusing
Muon loss
BG π contamination
Free from any of these

## Slide 7: Ultra-cold Muon
Requirement for zero E-field:
Muons should be kept stored without E-focusing
 Beam with ultra-small transverse dispersion,
i.e. ΔpT/p ~0
28MeV/c
3 keV/c
re-acceleration
300 MeV/c
p =
ΔpT/p ~3 keV / 300 MeV =1E-5
Laser resonant ionization of Mu (μ+e-)

## Slide 8
Production target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Silicon
Tracker
66 cm
Super Precision Storage Magnet
(3T, ~1ppm local precision)
Resonant Laser Ionization of Muonium (~106 m+/s)
Δ(g-2) = 0.1 ppm
ΔEDM = 10-21 e・cm

## Slide 9: Experimental sequence
40ms (25 Hz)
~1μs
40 μs
Surface
muon beam
(28 MeV/c)
Thermal
muonium
(3keV/c)
Ultra-slow muon
(3keV/c)
Acceleration + injection
(300 MeV/c)
Storage and detection
(300 MeV/c)
~1ns
~3ns
laser ionization
μ+e+
μ+
μ+
Mu
μ+

## Slide 10
Bird’s eye photo in Feb. 2008
J-PARC Facility
Material and Life Science
Facility
Neutrino Beam
To Kamioka
Main Ring
(30 GeV)
Hadron Hall
LINAC
3 GeV
Synchrotron
Beam energy: 3 GeV
Beam power : 1 MW (500 kW as of Jun 2018)
Intensity: 2E15 protons/sec
Repetition rate: 25 Hz (double bunches)

## Slide 11: Muon experimental facility (MUSE)
D-line
U-line
General purpose
（50 keV~50 MeV）,
(2009~)
Ultra slow beam
（0.1〜 30 keV）
(2016~)
µ+
µ±
S-line
Surface muon
（4 MeV）, (2014~)
µ+
H-line
Surface muon
for muon g-2/EDM
and Mu-HFS
(Under construction)
µ±

## Slide 12: Proposed experimental site
Parking lot
muon
production
target
sparation neutron
source
g-2/EDM
storage magnet
muon linac
H-Line
MuSEUM
DeeMe
Material and Life science Facility in J-PARC
New Electric
Power substation

## Slide 13: New electric sub-station for H-line
Cabling hole on the wall
Bedding for the sub-station
Pictures by T. Yamazaki

## Slide 14
2016.8.17

## Slide 15
branch
surface muon
mu LINAC
MuSEUM (Mu-HFS, μμ/μp)
DeeMe (mu-e conv.)

## Slide 16
Production target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Silicon
Tracker
66 cm
Super Precision Storage Magnet
(3T, ~1ppm local precision)
Resonant Laser Ionization of Muonium (~106 m+/s)
Δ(g-2) = 0.1 ppm
ΔEDM = 10-21 e・cm

## Slide 17
muon beam
Muonium
(m+e-)
Silica aerogel
（SiO2, 30 mg/cc）
Laser-ablated holes
8 mm
○ no hole
● w/ holes
P. Bakule et al., PTEP 103C0 (2013)
G. Beer et al., PTEP 091C01 (2014)

## Slide 18: Mu production experiment at TRIUMF (June-July, 2017)
Tested 25 samples in 3 weeks.
2/3rd of them were produced during run on the fly

## Slide 19: Long-term stability of Mu yield
TRIUMF-S1249
(Online data)
No hint of degradation observed for 2.5 days

## Slide 20: Muonium spin precession in vacuum
TRIUMF-S1249
(Online data)
Reconfirmed polarization of Mu in vacuum.

## Slide 21
Schematic of laser system
Slide by Satoshi Wada (RIKEN)

## Slide 22
Schematic of laser system
Slide by Satoshi Wada (RIKEN)
Lyman-α
guide laser
Generation of Lyman-α at J-PARC U-line
estimated energy = 8.4μJ (after LiF)
(design goal: 100μJ)

## Slide 23: Adopted technology for muon acceleration
Bunching
Section
High hunt impedance
External coupling structure for low-β
Similar to electron accelerator to obtain high gradient.
M. Otani et al., Phys. Rev. Accel. Beams 19, 040101 (2016)

## Slide 24: Muon RF acceleration for the first time!
J-PARC MLF D2 area, October 2017
Slide by M. Otani

## Slide 25: Muon RF acceleration for the first time!
J-PARC MLF D2 area, October 2017
Slide by M. Otani
S. Bae et al.,Phys. Rev. AB 21, 050101 (2018).

## Slide 26: An accelerating structure (IH-DTL cavity) to 1.3 MeV
Mar 2017, Photo by M. Otani

## Slide 27: A test of thin beam profile monitor at J-PARC (Feb 2018)
CsI(Tl) film
(3mm)
m+
Raw data
BINP-SNU-KEK

## Slide 28: Next step: re-acceleration to 1 MeV
Q-magnets
RFQ
IH
Mu
production
Beam
diagnostics
detectors
J-PARC MLF
Experimental Hall
Solenoid
Beam
Blocker
H1 area
(MuSEUM/DeeMe)
Bend
magnet
Q-magnets
blocker
surface muon (4 MeV)
accelerated muon (25meV1.3 MeV)
Initial
Accel.

## Slide 29: Next step: re-acceleration to 1 MeV
Q-magnets
RFQ
IH
Mu
production
Beam
diagnostics
detectors
Solenoid
Beam
Blocker
H1 area
(MuSEUM/DeeMe)
Bend
magnet
Q-magnets
blocker
surface muon (4 MeV)
accelerated muon (25meV1.3 MeV)
Initial
Accel.
Tested in 2016
Tested in 2016
Tested in 2016
Prototype
Tested in 2017
To be tested

## Slide 30: Muon beam injection and storage
Horizontal injection + kicker
(BNL E821, FNAL E989)
3D spiral injection + kicker
(J-PARC E34)
Injection efficiency : 3-5%(*)
(*) PRD73,072003 (2006)
Injection efficiency : ~85%
H. Iinuma et al., Nucl. Instr. And Methods. A 832, 51 (2016)

## Slide 31: Spiral Injection Test Experiment with low-energy electron beam
H. Iinuma (Ibaraki), M. A. Rehman (Sokenai)
beam energy: 112 keV
magnetic field: 102 G

## Slide 32: Muon storage magnet and detector
Cryogenics
e+ tracking
detector
2900 mm
Muon storage orbit
Iron yoke
Super conducting coils
666 mm
32
32
32
Drawn by Hitachi Co.
M. Abe et. al., Nuclear Inst. and Methods in Physics Research A 890, 51 (2018)

## Slide 33: Positron tracking detector
First working test module
tested in Mu-HFS experiment (June 2017)
KEK
Mechanical
Engineering
Center
A tracking detector ( vs. calorimeter)
  Robust against pileups
Partial funding available to construct a part of detector system

## Slide 34: Second-round with many improvements
ANL, March 27 2018

## Slide 35: TDR focused review (Nov 15-16,2016)
Oct 15, 2016 Technical Design Report (TDR) submitted
Nov 15-16, 2016 Review meeting
Dec 15, 2017 Responses from the collaboration submitted
May 25, 2018 Report from the committee
July 18-20, 2018 Approval will be discussed in the PAC meeting

## Slide 36
TDR
physics
data & results
construction
Squamish, BC (Canada)

## Slide 37: Technically-driven schedule and cost
Assumption : Major construction fund becomes available in JFY201X
(1.5 Oku secured by Grant-in-aids)

## Slide 38: Summary
We plan to measure muon’s g-2 and EDM with ultra-cold muon beam at J-PARC.
  Complemental & independent from BNL and Fermilab g-2 measurements
News since last year
  Oct. 2017, First muon acceleration to 90 keV
  Mar 2018, Cross calibration of NMR probes (J-PARC,Fermilab)
  April 2018, Major funding for construction of the upstream muon beamline is provided.
  May 2018, Received very positive replies from the TDR review committee (FRC)
  (July 2018), Waiting for full approval from the lab.