## Slide 1: First observation of the He+ 1S-2S transition in an atomic beam
LaserLaB, Vrije Universiteit Amsterdam,
Quantum Metrology and Laser Applications
Kjeld Eikema
ECTI November 2021
Funding:
LaserLaB, Vrije Universiteit Amsterdam,
Quantum Metrology and Laser Applications group
Kjeld Eikema
PREN Mainz, 26 June 2023

## Slide 2: Outline
  Introduction spectroscopy 1S-2S in He+
  Ramsey-comb spectroscopy (RCS)
  First 1S-2S excitation of He+ using an atomic beam (1 pulse)
  Comparison with TDSE simulations
  Conclusion and outlook for RCS of 1S-2S in He+
2

## Slide 3
Precision spectroscop on bound systems
H, mH, mHe+, H2, D2, HD, HT, H2+, HD+, He, He+...
Theory
CODATA
Fundamental
constants
(Trapped) particle measurements
mp/me , md/mp, a, ...
EDM (e & n) measurements,
and other methods
New
Physics?
3
Precision measurement for searching new physics
Black: pursued at LaserLaB Vrije Universiteit Amsterdam

## Slide 4
4
Precision measurement for searching new physics

## Slide 5: Possibilities 4He+ 1S-2S combined with H and m4He+
Experimental target 1S-2S in He+ is < 1 kHz
5
See: Krauth, J.J., Schuhmann, K., Ahmed, M.A. et al. Nature 589, 527–531 (2021)
Ry. test at 24 kHz
ra test at 60 kHz
QED test 41 kHz
With ra from m4He+
With current R♾ and slightly improved QED
With ra from m4He+ and Karshenboim PLB795 (2019)
Yerokin Ann. Phys. 531 (2019)
1S
2S
4He+
2P
l = 30 nm
(XUV)

## Slide 6: Frequency comb lasers
Frequency domain (averaged):
f0 and frep locked to atomic clock
Narrow and well defined modes

## Slide 7: Frequency comb lasers
Time domain (averaged):
attosecond pulse timing accuracy
sub-mrad phase evolution accuracy
Frequency domain (averaged):
f0 and frep locked to atomic clock
Narrow and well defined modes

## Slide 8: He+ 1S-2S spectroscopy – two approaches
8
1S
2S
4He+
2P
Munich, MPQ (Udem group)
Herrmann et al., PRA 79, 052505 (2009)
Moreno et al., Eur. Phys. J. D 77, 67 (2023)
2x 60 nm
Frequency domain approach
Time domain approach

## Slide 9: He+ 1S-2S spectroscopy – two approaches
9
1S
2S
790 nm
32 nm
2P
4He+
Amsterdam, LaserLaB (Eikema group)
Krauth et al., PoS (FFK2019) 353, 1 (2020)
Dreissen et al., PRL 123, 143001 (2019)
1S
2S
4He+
2P
Munich, MPQ (Udem group)
Herrmann et al., PRA 79, 052505 (2009)
Moreno et al., Eur. Phys. J. D 77, 67 (2023)
2x 60 nm
Frequency domain approach
Time domain approach

## Slide 10: The Ramsey-comb laser → power & precision
10
Cs
clock
Df phase measurement
upconversion & spectroscopy
two amplified FC pulses (5mJ)
pulse length fs – ps range
easy wavelength selection
av. phase constant at ~ 1 mrad
phase noise ~50 mrad for BBO, and 15 mrad expected for LBO
532 nm
10
Nat. Phys. 10, 30-33 (2014)
PRA 89, 052510 (2014)
PRL 117, 173201 (2016)
PRL 120, 043204 (2018)
PRL 123, 143001 (2019)
Mol. Phys. Accepted (2023)
LBO-based OPA

## Slide 11: Ramsey-comb spectroscopy – the principle
|g>
|e>
nano or microsecond delay: N Trep
1st
2nd
}
= DE
Dt = NDT + dt →
Excitation probability
Ramsey fringe recording
0

## Slide 12: Ramsey-comb spectroscopy – the principle
|g>
|e>
|g>
|e>
} A2 = p
nano or microsecond delay: N Trep
1st
2nd
Phase evolution ei 2p DE Dt /h
}
= DE
1st
2nd
Excitation probability
Ramsey fringe recording
p
0
Dt = NDT + dt →

## Slide 13: Ramsey-comb spectroscopy – the principle
|g>
|e>
|g>
|e>
} (2A)2 = 4p
|g>
|e>
} A2 = p
nano or microsecond delay: N Trep
1st
2nd
Phase evolution ei 2p DE Dt /h
}
= DE
Excitation probability
1st
2nd
2nd
Ramsey fringe recording
Dt = NDT + dt →
Signal ~ 1+ cos (2p ftrans Dt + Df)

## Slide 14: Ramsey-comb spectroscopy – the principle
|g>
|e>
|g>
|e>
} (4A)2 = 4p
|g>
|e>
} A2 = 0
|g>
|e>
} A2 = p
dt
attosecond micro-delay by adjusting frep
nano or microsecond delay: N Trep
1st
2nd
Phase evolution ei 2p DE Dt /h
}
= DE
Excitation probability
1st
2nd
2nd
2nd
Ramsey fringe recording
Dt = NDT + dt →
Signal ~ 1+ cos (2p ftrans Dt + Df)
4p

## Slide 15: Ramsey-comb spectroscopy – the principle
Transition frequency
tp = pulse length (square pulses)
WR = Rabi frequency (depends on intensity)
b = Rabi frequency with detunig taken into account
Df = detunig center of pulse spectrum
* see PRA 89, 052510 (2014)
tr
Excitation probability after 2 identical pulses*:

## Slide 16: Ramsey-comb spectroscopy – the principle
Transition frequency
tp = pulse length (square pulses)
WR = Rabi frequency (depends on intensity)
b = Rabi frequency with detunig taken into account
Df = detunig center of pulse spectrum
* see PRA 89, 052510 (2014)
tr
Excitation probability after 2 identical pulses*:

## Slide 17: Solution: Ramsey-comb spectroscopy – macro delays
What to do about the unknown Df ?
Nat. Phys. 10, 30-33 (2014)
PRA 89, 052510 (2014)
Signal ~ 1+ cos (2p ftrans [Trep+dt] + Df)
Ramsey signal

## Slide 18: Ramsey-comb spectroscopy – macro delays
Pure relative phase analysis gives ftransition!
Suppression of common mode phase shifts, including AC-Stark shift
Change macro delay by taking different FC pulses
Nat. Phys. 10, 30-33 (2014)
PRA 89, 052510 (2014)
Signal ~ 1+ cos (2p ftrans [Trep+dt] + Df)
Ramsey signal

## Slide 19: Ramsey-comb spectroscopy – macro delays
Nat. Phys. 10, 30-33 (2014)
PRA 89, 052510 (2014)
Pure relative phase analysis gives ftransition!
Suppression of common mode phase shifts, including AC-Stark shift
Longer delay gives better accuracy & resolution
Change macro delay by taking different FC pulses
Signal ~ 1+ cos (2p ftrans [NTrep+dt] + Df)
Ramsey signal

## Slide 20: The plan: Ramsey-comb excitation of He+ 1S-2S in a trap
20
He+
Be+
32 nm +
790 nm
32 nm +
790 nm
1S
2S
He+
790 nm
32 nm
2P

## Slide 21: 1st order Doppler cancellation by synchronization
21
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 22: 1st order Doppler cancellation by synchronization
22
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 23: 1st order Doppler cancellation by synchronization
23
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 24: 1st order Doppler cancellation by synchronization
24
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 25: 1st order Doppler cancellation by synchronization
25
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 26: 1st order Doppler cancellation by synchronization
26
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
fsec = 5 MHz
Recoil =55 MHz

## Slide 27: 1st order Doppler cancellation by synchronization
27
Movement ion periodic with fsec and fRF
→ Match Trep of laser to Tsec and TRF
He+
Spectroscopy accuracy depends on
accuracy synchronization,
recoil from 32+790 nm
vibrational state occupation
harmonicity
Lock at 10-4 → 11 kHz
fsec = 5 MHz
Recoil =55 MHz

## Slide 28: 1st order Doppler cancellation by synchronization
28
Resonator with tuning and RF amplitude stabilisation
Ion trap, collaboration with Tanja Mehlstäubler (PTP)
313 nm laser cooling

## Slide 29: XUV (frequency comb) generation
XUV light
>1013 W/cm2
29

## Slide 30: XUV (frequency comb) generation
UV – XUV comb
>1013 W/cm2
30
Electric field of light (orange line) deforms Coulomb potential atoms in the jet
Nature Physics 3, 381 (2007)
PRL 71, 1994-1997 (1993).
PRA 49, 2117-2131 (1994).
1: tunneling
2: acceleration
3: recombination
‘simple man’ Three step model

## Slide 31: XUV (frequency comb) generation
UV – XUV comb
Harmonic orders
NIR comb
f = fceo + n frep
f = p fceo + m frep
f0
>1013 W/cm2
Int.
Int.
XUV comb
pth
harmonic
31

## Slide 32: Xe experiment to test (ionization) phase effects HHG
5p6
5p5 8s
(t=24 ns)
Xe
1064 nm
110 nm
(7th harm.)
Argon jet

## Slide 33: First demonstration of RCS with HHG, in Xe at 110 nm
Xe @ 110 nm
Phase effects quickly diminish to few mrad in tens of ns at 0.8 ⨉ 1014 W/cm2
Enabled most accurate spectroscopy to date with HHG: dn/n = 2.3 ⨉ 10 -10
HHG power 2nd pulse recovers after 100 ns (transit of Ar)
L.S. Dreissen et al.,
PRL 123, 143001 (2019)
L.S. Dreissen et al.,
PRA 101, 052509 (2020)
Contrast reduction:
- Transit time
- 8s lifetime of 23 ns
- Doppler

## Slide 34: What does this mean for He+ 1S-2S?
kHz-level accuracy possible at 30 nm for microseconds pulse delay
NIR phase noise has to stay < 40 mrad over a few microseconds (contrast): possible
Negligible phase shift due to HHG process (pulse delays > 100 ns)
No time-of-flight limitation as we had with Xe
...

## Slide 35: Single-pulse excitation of He+ in an atomic beam
Excitation
1S - 2S He+
Ionization
He to He+
Ionization
2S He+ to He2+
HHG
NIR (790 nm)
150 fs
time
intensity
Enables to test all aspects of generation, excitation, and detection of He+
Excitation probability only 4x lower than 2-pulse RCS & trapping
Total experiment done in 150 fs...

## Slide 36: 3He+ 1S-2S excitation setup
3He to avoid H2+ background signal
XUV, + NIR power adjustment with iris

## Slide 37: High-harmonic generation spectrum
NIR pulse 1 mJ, 150 fs
f=30 cm focusing to 33 mm FWHM
32 nm right at HHG cutoff
resolution limited by spectrometer
HHG in argon
XUV beam
after int. zone

## Slide 38: He+ generation by ionization He with 17th harm.
up to 150 He+ ions per laser pulse
great news for ion trap loading; low intensity He beam possible

## Slide 39: First 1S-2S excitation of He+
Massive ac-Stark shift from NIR intensity (max. 50 THz on the 1S - 2S)
Excitation probability ~ 10-4 per pulse of NIR+XUV → 10-3 expected for RCS (2 pulses)
Saturation effects visible
Excitation probabilty, He2+ det.
Center NIR wavelength (nm)
NIR intensity in 1014 W/cm2

## Slide 40: Is this really pure 1S-2S excitation?
ac-Stark shift from NIR
He2+ signal vs. 32 nm harmonic
Strongly suggests 1S-2S:
2P excitation would extrapolate to 760 nm
Only 1 photon at 32 nm is involved,
and without NIR: no signal

## Slide 41: Is this really pure 1S-2S excitation?
ac-Stark shift from NIR
He2+ signal vs. 32 nm harmonic
Strongly suggests 1S-2S:
2P excitation would extrapolate to 760 nm
Only 1 photon at 32 nm is involved,
and without NIR: no signal
Experiment: 789.95(18) nm
Theory: 789.842 nm
accuracy: 2.2 * 10-4 😉

## Slide 42: TDSE simulation
HHG field simulation by Andrés Martinez de Velasco
Central wavelength NIR beam
Central wavelength NIR beam
Experiment
TDSE simulation
Integration step 0.5 attoseconds
TDSE simulation by Richard Taieb (Sorbonne, UPMC, Paris)

## Slide 43: TDSE simulation – resonance height and width
Trends the same: for high NIR power the resonance signal saturates
Resonance height (scaled to experiment)
Resonance width

## Slide 44: TDSE simulation – 2S, 2P, and He2+ population
States other than 2S at least 1000x less excited!
NIR dependence gives nice opportunity to control ionization detection without strong inpact on excitation
NIR @ 0.35x1014 W/cm2
NIR @ 1.00x1014 W/cm2
2P
2S
2S
2P
He2+
He2+

## Slide 45: TDSE simulation – 2S, 2P, and He2+ population
States other than 2S at least 1000x less excited!
NIR dependence gives nice opportunity to control ionization detection without strong inpact on excitation
NIR @ 0.35x1014 W/cm2
NIR @ 1.00x1014 W/cm2
2P
2S
2S
2P
He2+
He2+

## Slide 46: TDSE simulation – interesting time dynamics
Envelope NIR field
1-1S
2P
3P
2S
NIR at 791 nm and 0.35x1014 W/cm2
Strong mixing to P states, which disappears when NIR → 0
2S appears when 25th harmonic is generated

## Slide 47: TDSE simulation – interesting time dynamics
0.075 % in 2S
0.005 % He2+
‘Low’ NIR power
0.35x1014 W/cm2

## Slide 48: TDSE simulation – interesting time dynamics
0.03 % in 2S
0.1 % as He2+
‘High’ NIR power
0.8x1014 W/cm2

## Slide 49: 20 THz ac-Stark shift – precision spectroscopy?
ac-Stark shift of Df = 20 THz on 1S-2S at 0.35 x 1014 W/cm2
1S-2S He+
20 THz
Dw = Df/Dt
In RCS the NIR pulse has longer influence than 30 fs; ~5x more = 19 rad
Shift proportional to pulse energy, with 0.1% dependence on N
So remaining effect in RCS = 19 rad x 0.1% = 19 mrad
Leads in total to ~ 7.6 kHz error for 400 ns time delay in RCS (and scales down with 1/DT)
Comes from 3.8 rad in 30 fs (XUV generation window)

## Slide 50: 20 THz ac-Stark shift – precision spectroscopy?
ac-Stark shift of Df = 20 THz on 1S-2S at 0.35 x 1014 W/cm2
1S-2S He+
20 THz
Dw = Df/Dt
In RCS the NIR pulse has longer influence than 30 fs; ~5x more = 19 rad
Shift proportional to pulse energy, with 0.1% dependence on N
So remaining effect in RCS = 19 rad x 0.1% = 19 mrad
Leads in total to ~ 7.6 kHz error for 400 ns time delay in RCS (and scales down with 1/DT)
Comes from 3.8 rad in 30 fs (XUV generation window)

## Slide 51: Thanks to the Ramsey-comb He+/H2 team!
TDSE calculations (Paris, Sorbonne):
Richard Taieb
Elmer
Gründeman
Charlaine
Roth
Mathieu
Collombon
Julian
Krauth
KE
Laura
Dreissen
Vincent
Barbé
Andrés Martinez de Velasco
Collaboration for ion trap He+ with PTB:
Tanja Mehlstäubler and group members,
& Piet Schmidt
Alejandra Dias

## Slide 52: Summary
RCS successfully combined with HHG; Xe spectroscopy at 110 nm with 2.3 x 10-10
Demonstrated first 1S-2S excitation of He+
Excitation scheme 32 nm + 790 nm, with ionization control
1-pulse excitation probability 10-4; for RCS 10-3 expected
Other states like 2P excited at least a 1000x less
ac-Stark shift small enough for (sub)-kHz precision
TDSE simulations confirm 1S-2S excitation
1S-2S He+

## Slide 53: Outlook
Extensive TDSE simulation of full RCS excitation
Measure the phase (noise) of new RCS laser based on LBO
Install the ion trap with electronics and mechanics in the coming months
Followed by: demonstration of fast loading He+ and Be+
And then ... a precision 1S-2S measurement at 20 kHz accuracy! (hopefully)

## Slide 54: Extra slides
54

## Slide 55: Outlook on (initial) accuracy: < 20 kHz on 1S-2S
Contrast effects up to few ms time scale
RC laser induced phase noise: 40 mrad * 26th harm. = 1.1 rad in XUV = 1/6 of an optical cycle; OK
Vibrations (turbo’s): < 1 nm (random) = 0.2 rad = 1/30th of a cycle; ok
HHG induced phase noise: ~ 0.2 rad = 1/30th of an optical cycle; ok
ac-Stark shift phase noise: ~ 20 mrad; no issue
Systematics at initial Ramsey-comb DT=400 ns Error: Scaling:
Syncing Trep with Tsec and Tmicr at level of 10-4
NOPCPA phase shift accuracy < 1 mrad @ 790nm
ac-Stark on 1S-2S for 0.1% dependence 790 nm pulse energy on N
HHG differential phase
Thermal drift effects
11 kHz DT independent
10 kHz 1/DT
9 kHz 1/DT
4 kHz 1/DT
<< kHz DT
So an initial accuracy expected of <20 kHz

## Slide 56: Outlook on (initial) accuracy: < 20 kHz on 1S-2S
Contrast effects on RCS signal for up to few ms pulse time delay
Laser noise expected: 40 mrad * 26th harm. = 1.1 rad in XUV; OK: 1/6 of an optical cycle) @ 30 nm
Vibrations (turbo’s): < 1 nm (random) = 0.2 rad = 1/30th of a cycle; ok
ac-Stark phase shift noise (I@0.1%): < 0.01 rad in XUV; no problem
HHG phase noise 0.2 rad = 1/30th of a cycle.
Effects reduced by sync Trep with Tsec and Tmic at level of frac = 10-4
Systematic error from recoil: Df = h frac / (m l2) = 11 kHz
Ion temperature: < 1 nm random phase shift; no serious contrast loss or shift
Thermal: << 1 nm; systemati phase shift, but drops mostly out in RCS and is initially negligible
So an initial 1S-2S measurement accuracy of <20 kHz is expected
OPA differential phase effects: <1 mrad accuracy at 790nm, gives a 1S-2S shift of <10 kHz
HHG differential phase effects (I@0.1%): < 20 mrad at 32nm, gives 1S-2S shift of <4 kHz
ac-Stark differential phase (I@0.1%): < 20 mrad at 32nm, gives 1S-2S shift of <9 kHz
Thermal: < 0.1 pm (systematic, 20 mrad phase): can for the moment be neglected
Other systematics RCS with DT = 400 ns

## Slide 57: How to measure proton size rp and Rydberg with H?
R. Pohl et al., Metrologica 54, L1 (2017)
Measure ratios to determine and rp
H
Bohr
QED, Rel. etc
Nuclear size

## Slide 58: 2010-2013: conflicting proton radii
Randolf Pohl et al. Nature, vol. 466, pp. 213-216 (2010)
Measurement 2S-2P @ 6 mm of muonic hydrogen: 4% smaller proton?
Picture above from Science 339, 417-420 (2013). Many more publications followed
@ PSI
Muonic H spectroscopy
2S-2P at 6 mm
‘Normal’ H spectroscopy
& electron scattering
Nature 2010
58

## Slide 59: 2022: Still some confusing/intriguing results
59
Measurement of the 2S1/2 – 8D5/2 transition in hydrogen
Phys. Rev. Lett. 128, 023001 (2022)
A.D. Brandt et al. (group D. Yost)
Colorado State University & Russian Quantum Center
59

## Slide 60: Single pulse
Int.
0
frequency
60

## Slide 61: Frequency comb lasers: repetition
Int.
0
fn = fceo + n.frep
...
...
frequency
61

## Slide 62: Equal pulse distortion = OK!
Int.
0
fn = fceo + n.frep
Phases and intensities changed, but frequencies at the same position!
Photonic or holey fiber broadening
...
...
62

## Slide 63: Equal pulse distortion = OK!
Int.
0
fn = fceo + n.frep
Phases and intensities changed, but frequencies at the same position!
...
...
frequency
63

## Slide 64: High-harmonic generation (HHG)
Picture from: Corkum & Krausz, Nature Physics 3, 381 (2007)
Coulomb potential periodically deforms by electric field of light (orange line)
Corkum, P. B. Phys. Rev. Lett. 71, 1994-1997 (1993).
Lewenstein, M. et al. Phys. Rev. A 49, 2117-2131 (1994).
1: tunneling
2: acceleration
3: recombination
‘simple man’ Three step model
64

## Slide 65: HHG: periodic electron wavepacket recollision
The situation with a NIR fundamental beam and low ionization:
D. Popmintchev ... T. Popmintchev, Science 350, 1225-1231 (2015)
Murnane and Kapteyn group
65

## Slide 66: Long and short quantum paths
¾ optical period
¼

Krausz & Ivanov Rev. Mod. Phys. 81, 163 (2009)
3.2 Up
Max. electron energy:
(‘pondoromotive energy’)
Max. photon energy:
Ip = ionization potential of the atoms
El = electric field laser
Il = laser intensity
l = wavelength laser
w = ang. freq. laser
66

## Slide 67: HHG phase stability / coherence
Phase of emission:
q=harm. order
Action "S", depends on momentum p, which in turn depends on laser intensity
For plateau harmonics
Kshort ~ 0.3
Klong ~ 2.9
Keep the intensity stable (~1%), then the XUV phase is too!
(and use the short quantum path: also less divergent)
Emission time
(laser phase)
'Action'
(laser intensity)
R. Zerne et al.,
PRL 79, 1006 (1997)
2 HHG sources interfere: high coherence
67

## Slide 68: From harmonics to an XUV comb
Short-term periodic emission = harmonics in frequency domain Looks a bit like a frequency comb! (but not quite)
Emission twice per fundamental period, with p phase shift per emission: only odd harmonics produced: 3rd, 5th, 7th ...
Fundamental intensity
Each fundamental pulse
generates a train
of XUV pulses
Harmonic orders
Freq.
Int.
68

## Slide 69: When repeated for each comb pulse: XUV comb
Short-term periodic emission = harmonics in frequency domain Looks a bit like a frequency comb! (but not quite)
Emission twice per fundamental period, with p phase shift per emission: only odd harmonics produced: 3rd, 5th, 7th ...
Dipole phase tightly linked to fundamental driving field for each wavelength at ‘constant intensity’ (energy per pulse) of the fundamental
Maintains repeatability, so will upconvert frequency combs faithfully! (apart from noise power; that scales up quadratically).
Coherent emission per wavelength for equal fundamental intensity
Fundamental intensity
Each fundamental pulse
generates a train
of XUV pulses
...
...
Harmonic orders
f = p fceo + m frep
pth
harmonic
Freq.
Int.
69

## Slide 70: Phase measurement setup
CMOS image
reference pulses (FC pulse train)
amplified pulses
Pulse picking
Swapping

## Slide 71: Example: Ramsey XUV spectroscopy with 2 FC pulses
time
φCE= p/2
φCE= 0
T
frequency
Int.
0
fn = f0 + n.frep
frep = 1/T
f0 = frep x φCE / 2
Only 2 pulses from comb amplified to mJ level and upconverted
D. Kandula et al. PRL 105, 063001 (2010)
71

## Slide 72
time
φCE= p/2
φCE= 0
T
frequency
Int.
0
fn = f0 + n.frep
frep = 1/T
f0 = frep x φCE / 2
Only 2 pulses from comb amplified to mJ level and upconverted
Yikes, true repetition violated!
D. Kandula et al. PRL 105, 063001 (2010)
72
Example: Ramsey XUV spectroscopy with 2 FC pulses

## Slide 73: Ramsey XUV spectroscopy with 2 FC pulses
121 MHz
D. Kandula et al. PRL 105, 063001 (2010)
D. Kandula et al. PRA 84, 062512 (2011)
Dominik Kandula
Christoph Gohle
Accuracy: 6 MHz
Limitation:
Phase shifts between the pulses
from amplification and HHG.
HOW TO SOLVE THIS?
Helium 1 1S0 – 5 1P1 transition
at 51 nm (15th harmonic)
73

## Slide 74: X-EF para-H2 Ramsey-comb spectroscopy at 2x 202 nm
Pure H2
Contrast: 78% 51% 31%
Contrast: 72% 56% 47%
Mixture H2/Ne (slow beam)
Accuracy X-EF transition for para* H2 (N=0) 30 kHz,
and for D2 (N=1) 19 kHz ; paper submitted February 2023
Charlaine Roth
* Para H2: nuclear spins anti-parallel. Ortho-H2: nuclear spins parallel.
Andrés Martinez de Velasco

## Slide 75
Pure H2
Contrast: 78% 51% 31%
Contrast: 72% 56% 47%
Mixture H2/Ne (slow beam)
Accuracy X-EF transition for para* H2 (N=0) 30 kHz,
and for D2 (N=1) 19 kHz ; paper submitted February 2023
Charlaine Roth
* Para H2: nuclear spins anti-parallel. Ortho-H2: nuclear spins parallel.
Andrés Martinez de Velasco
Poster by Andrés Martinez de Velasco
X-EF para-H2 Ramsey-comb spectroscopy at 2x 202 nm

## Slide 76: Influence of ionization during HHG: intensity
Intensity effect from loss of neutral atoms and disrupted phase-matching
VUV Intensity pulse 2 / pulse 1
New atoms need to fly in HHG zone which takes ~ 50-100 ns
VUV yield 7th harmonic in Ar at 110 nm
76
Time =(DN*8ns)

## Slide 77: Phase influence of the HHG process in argon
Phase difference pulses measured with Xe Ramsey signal, relative to phase for DN=2 (=16 ns)
Fast & large phase effect from electrons
Slow & small phase effect from ions
L.S. Dreissen et al., PRA 101, 052509 (2020)
At 0.8x1014 W/cm2 effect only few mrad in the VUV
L.S. Dreissen et al., PRL 123, 143001 (2019)
W/cm2

## Slide 78: Absolute calibration for 110 nm xenon transition
L.S. Dreissen et al., PRL 123, 143001 (2019)
L.S. Dreissen et al., PRA 101, 052509 (2020)
Most accurate frequency measurement with a HHG source:
dn/n = 2.3 ⨉ 10 -10
Improvement 10 000⨉ relative to previous measurement:
Yoshino et al., J. Opt. Soc. Am. B 2, (1985)
300 measurements
nAr(8S) = 2726086012473(630) kHz

## Slide 79: Low-phase noise Ramsey-comb laser, No. 2
New Ramsey-comb laser ready after 4 years of development
2 times 5 mJ amplified pulses @ 28 Hz, 10 - 20 nm bandwidth, 1 % rms energy stability
Still to check: target phase noise <40 mrad in total for microsecond pulse delay
Charlaine Roth
Mathieu Collombon
Pump laser
Vincent Barbé
Bounce amp & ULN Comb laser
New parametric amplifier

## Slide 80: Overview vacuum setup for He+
80
spectrometer
He and He* beam
Detection platform
6-D trap adjustment
Toroidal mirror chambers
High-harmonic generation
NIR adjustment and XUV filtering
Laser cooling
platforms

## Slide 81: Planar trap and light collection from Be+ ion

## Slide 82: Ion trap in collaboration with PTB Germany
Segmented Paul trap with micromotion compensation.
Separate loading and spectroscopy zones
Collaboration with PTB (T. Mehlstäubler and P. Schmidt) for the design
Comp. chip
RF chip
RF chip
Comp. chip
Carrier board
RF ~ 40 MHz wsec (He+) ~ 5 MHz

## Slide 83: Ion trap built at PTB
Design modified/built by Elmer Gründeman (VU) with generous help from the group of Tanja Mehlstäubler (PTB)
(a.o. Malte Brinkmann)
Be+ and He+ in trap

## Slide 84: XUV beam fixed; ion trap movement 6 DOF
Julian
Krauth
Test ion trap movement and 313 nm detection
13 motors to control 6 degrees-of-freedom for trap and fluorescence detection
Stability/resolution ~1 micrometer long term and sub-nm for 10’s of microseconds confirmed
Diffraction-limited Be+ 313 nm detection with double-aspheric lens (NA=0.5)

## Slide 85: Many more components now ready
To trap
RF in
Capacitive tuner
Heating resistors
RF power stabilisation
Trap-voltage amplifiers
Combined with ARTIQ hardware
TDC micromotion detection
313 nm Be+ laser
with all beams for sideband cooling

## Slide 86: Motivation for He+ 1S-2S spectroscopy
86
1S
2S
4He+
2P
86
Hydrogen-like system: calculable (Pachucki et al.)
Test fundamental physics; obtain a consistant picture
QED and nuclear size effects bigger in He+ than H
Can be trapped in a Paul trap for long observation
Compare with mHe+ measurements
See: J.J. Krauth et al. Nature 589, 527–531 (2021) & arXiv (2023)
(NS = nuclear size, charge)
l = 30 nm: extreme-ultraviolet
(XUV)
1.9 ms
(84 Hz)

## Slide 87: Ramsey (comb) spectroscopy – the principle
|g>
|e>
Phase evolution ~ ei 2p DE Dt /h
DE
Dt
Probe phase evolution of the excited superposition with amplified frequency comb pulses
high timing and phase accuracy
easy upconversion
high probability excitation
efficient detection – short time window
‘isolation’ from environment noise
broad bandwidth: we always hit the transition
Two amplified FC pulses
Subtle differences with ‘normal’ Ramsey spectroscopy:
Norman Ramsey, Phys. Rev. 76, 996 (1949)
Norman Ramsey, Phys. Rev. 78, 695 (1950)
}
Atomic states

## Slide 88: The plan: Ramsey-comb excitation of He+ 1S-2S in a trap
88
He+
Be+
32 nm +
790 nm
32 nm +
790 nm
1S
2S
He+
790 nm
32 nm
2P

## Slide 89: General approach 1S-2S transition in trapped He+
Ar jet
lens
32nm + 790 nm Ramsey-comb pulses
NIR Ramsey-comb near 790 nm
frequency
comb laser
Cs
atomic
clock
XUV mirror
toroidal pair
Be+ cooling
laser 313 nm
2-pulse
amp.
HHG
He+
Be+
EMCCD 313 nm
detection
Extra
laser(s)
Planar ion trap.
Collaboration with
Tanja Mehlstäubler
& Piet Schmidt from PTB Germany
Sub-Hz
laser
Reference
cavity
89

## Slide 90: What about the 1st order Doppler effect?
Loading and sympathetic cooling
Be+
He2+
Be+
He+
Be+
He+
Not excited
If He2+ then Be+ moves
1S-2S He+ excited
Be+
He+
Relax trap axially, &
lock He+ movement radial frequency fsec & fmic (single trap mode) to Trep
RCS 1S-2S excitation
+ 2S ionizaton
Synchronize ion (1 He+!) movement with the Ramsey-comb excitation pulses: no first-order Doppler
Spectroscopy accuracy depends on
accuracy synchronization,
recoil from 32+790 nm
vibrational state occupation
Lock at 10-4 → 11 kHz
}
Be+
He+
313 nm
313 nm