## Slide 1
Advancing Time Synchronization for Global Quantum Sensing: From GNOME Insights to the GravNet Cavity‑Network Framework
Daniel Gavilán and Oleg Tretiak
26.06.2025

## Slide 2: Two general ways of time synchronization
“Dual Link”
“Passive”
Network Time Protocol (NTP)
    Bad accuracy (> 1us). Useful for computer time synchronization
IEEE1588 (PTP)
  White rabbit
    Very good accuracy (< 1 ns)
    Short synchronization distances (10km)
    Requires “almost” direct connection
Two-way satellite time and frequency transfer (TWSTFT)
    Good accuracy (about 1 ns) .
    Long synchronization distances
    Extremely expensive (> 100K)
Global Navigation Satellite System (GNSS)
  Good accuracy (30ns) for many application (first navigation).
  Relatively cheap
  Affected by many factors (atmospheric phenomena, building, cables length, electronic warfare systems etc..)
  Now way to monitor signal delay

## Slide 3: GNOME DAQ system
Włodarczyk, P., Pustelny, S., Budker, D., & Lipiński, M. (2014). Multi-channel data acquisition system with absolute time synchronization. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 763, 150-154.

## Slide 4: GNOME DAQ system
Włodarczyk, P., Pustelny, S., Budker, D., & Lipiński, M. (2014). Multi-channel data acquisition system with absolute time synchronization. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 763, 150-154.
4 channels
16-bit analog-to-digital converter ADS8507
1 kSample/second data rate
Data logging on SD card (1-Minute-long files)

## Slide 5: Timestamping the data with pulse per second (PPS)
1
0
0
…
1
1
0
1
0
0
…
1
1
1
ADC 0
1
0
0
…
1
1
1
ADC 1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
Data frame
1
0
0
0
0
0
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
0
0
0
0
0
0
1
GNSS PPS
1
0
0
…
1
1
1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
Add time Bit on top of ADC readings
Data could be recovered if it is corrupted

## Slide 6: Inter-range instrumentation group (IRIG-B) timecode

## Slide 7: IRIG-B timecode

## Slide 8: Timestamping the data with IRIG-B
1
0
0
…
1
1
0
1
0
0
…
1
1
1
ADC 0
1
0
0
…
1
1
1
ADC 1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
1
0
0
0
0
0
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
0
0
0
0
0
0
1
GNSS PPS
1
0
0
…
1
1
1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
0
1
0
0
…
1
1
1
1
0
0
…
1
1
1
Time code
Add time Bit and IRIG-B code on top of ADC readings
Data could be fully recovered if it was corrupted

## Slide 9: PRESISION TIME REFFERENCE

## Slide 10: Commercial Daq cards with timestamp
M2p.59xx-x4 PCI Express
ADQ7DC

## Slide 11: Commercial Daq cards with timestamp
M2p.59xx-x4 PCI Express
ADQ7DC

## Slide 12: Data on demand Model
I have signal! Take my data! Do others see it?
Station 1
Station 2
Station 3
Data center

## Slide 13: Data on demand Model
I have signal! Take my data! Do others see it?
Station 1
Station 2
Station 3
Data center

## Slide 14: Data on demand Model
Provide me the data for 2:23:45 PM
Station 1
Station 2
Station 3
Data center
Provide me the data for 2:23:45 PM

## Slide 15: Data on demand Model
Take data for 2:23:45 PM
Station 1
Station 2
Station 3
Data center
Take my data 2:23:45 PM

## Slide 16: Data on demand Model
Take data for 2:23:45 PM
Station 1
Station 2
Station 3
Data center
Take my data 2:23:45 PM

## Slide 17: Data on demand Model
Station 1
Station 2
Station 3
Data center
Corrupted data with timestamps can be reconstructed

## Slide 18
Thank you!

## Slide 19: Network Time Protocol (NTP)
  ⏱ Precise Time Synchronization
      Synchronizes clocks across networks with millisecond accuracy (or better).
  🌐 Hierarchy with Stratum Levels
      Tiered time sources (Stratum 0 to Stratum 15) ensure redundancy and trustworthiness.
  🔁 Continuous Adjustment, Not Jumps
      Gradually corrects time via slewing to avoid abrupt system changes.
  🧭 Round-trip Delay Compensation
      Accounts for network latency to improve accuracy.
  🔒 Authentication Support
      Can verify time source authenticity to prevent spoofing (e.g. using symmetric keys or Autokey).

## Slide 20: Precision Time Protocol (PTP)
⏱ Sub-microsecond accuracy
  Provides synchronization precision in the nanosecond to microsecond range — ideal for industrial, financial, and telecom systems.
🌐 Master–Slave Architecture
  A Grandmaster clock distributes time to slaves via hierarchical or peer-to-peer setups.
📡 Hardware Timestamping Support
  Works with network interface cards (NICs) or dedicated hardware to capture timestamps at the physical layer — boosts precision.
🔁 Delay Measurement & Compensation
  Uses two-way message exchange to measure propagation delay and compensate for it in real time.
🧩 Profiles for Specific Industries
  Customizable via PTP profiles (e.g., telecom, power systems, finance) that define timing behavior and accuracy requirements.
🧭 Boundary and Transparent Clocks
  Specialized network devices that help correct or forward timing information without degradation — key in large or switched networks.
🔒 Security Still Emerging
  Less mature than NTP in terms of security; standards like IEEE 1588-2019 are addressing this with new protections.

## Slide 21: White rabbit
⏱ Sub-nanosecond Accuracy
  Synchronizes clocks with <1 ns precision — far beyond standard PTP. Crucial for experiments, time-critical measurement systems, and high-frequency trading.
🔌 Based on IEEE 1588 (PTP) + SyncE
  Combines Precision Time Protocol (PTP) with Synchronous Ethernet (SyncE) to achieve ultra-stable frequency and phase alignment.
🧭 Fixed Path Delay Measurement
  Uses precise calibration of fiber lengths and deterministic switching to eliminate jitter and latency variability.
🧬 Deterministic Timing
  Guarantees fixed and predictable latency, critical for scientific instrumentation and real-time systems.
🔁 Real-time Delay Compensation
  Continuously measures and compensates for signal delay variations (e.g., due to temperature-induced fiber changes).
🛠 Open Hardware + Open Source
  Developed at CERN; designs and firmware are openly available for research and industrial use.
🧩 Used in Large-Scale Distributed Systems
  Powers timing at facilities like CERN's particle accelerators, radio telescopes, and smart grids.

## Slide 22: Two-Way Satellite Time and Frequency Transfer (TWSTFT)
🔁 Two-Way Time Transfer via Satellite
  Simultaneous exchange of timing signals between two ground stations using the same satellite — minimizes asymmetrical delays.
⏱ High Precision (few ns)
  Achieves ~1–2 nanosecond accuracy, making it ideal for atomic clock comparison, metrology labs, and GNSS validation.
🧭 Delay Calibration Built-in
  Because both stations send and receive, propagation delay is measured directly and compensated, improving accuracy over one-way systems.
🛰️ Satellite Link Dependency
  Requires leased transponder time on geostationary satellites — high cost and infrastructure needs.
🧪 Used in Time Metrology and Standards
  Key method for comparing time between national metrology institutes (NMIs) and maintaining UTC (alongside GNSS and optical fiber).
📶 Carrier-Phase Techniques
  Advanced variants use carrier-phase measurements for even higher precision over longer time baselines.
🧷 Robust Against Interference
  Independent of internet or local infrastructure; more resistant to network-related timing issues.