## Slide 1: Cosmic Ray Trigger V4
Svoboda, ANNIE CM February 2026

## Slide 2
Summed output on the back of each CAMAC discriminator
There are twelve layers in z, with each layer having two discriminators and one TDC
Each discriminator has a 1 mA/hit = 50 mV/hit into 5-0 ohms
Summed output that can be daisy chained

## Slide 3
CR Trigger
Version 3
summing
amplifiers

## Slide 5
Some paddles have noisy/oscillating
discriminators when registering a large
pulse.
Since every paddle has an equal vote
in the trigger coincidence sum, we are
very sensitive to such noise.
Most the the CR triggers are noise
instead of useful data

## Slide 6
Solution: Move to a trigger where each layer
gets one “vote” no matter how many paddles
in the layer fired.

## Slide 7
Layer 0
vote
Layer 1
vote
Layer 10
vote
Layer 11
vote
…
Layer 2
vote
Each vote is a -1 V logic
pulse from the
layer discriminator
x12
…
x12
-0.20 V
max
Each of the 4 layers are analog
summed such that the max
output is -0.8 V (within spec)
LRS Model 428 Quad Linear Fan-In/Fan-Out
7 dB
3dB
-0.4 V max
3dB
3dB
-1.2 V max
1 paddle
= 100 mV
to CR trigger
discriminator

## Slide 8: What do we need?
twelve 7 dB attenuators + spare
three 3 dB attenuators + spare
12 channels of layer discriminators (2 octal NIM discriminators)
1 channel of CR discriminator
1 NIM Quad Linear FIFO
BNC/lemo adapters

## Slide 9: When to do this?
Do not have to stop beam data taking when setting up, but should plan on a day of testing before bringing online
Will need to take scaler rates of layers and CR overall sum to set the thresholds
What CR trigger rate can we handle?
March 31-April 2 time frame?