Investigation of the front end electronics
for the proton radius experiments
Alexander Inglessi • PNPI Gatchina
TPC Collaboration Meeting • 10 March 2020 • TU Mainz

---
TPC prototype
Active target: gas target + ionization chamber

---
Front-end prototype

---
SIS3316 VME digitizers
- 16 channels per module
- 25 MHz (40 ns bin),
  up to 250 MHz
- 14 bit, 5 V (2 V) range
- Int./ext. trigger
- MAW energy/threshold

---
Individual signal analysis
- Signal smoothing
- Peak search
- Obtaining time parameters by slope differentiation
- Pedestal correction
- Peak raw signal integration → energy

---
Recoil track search
- Initial algorithm implementation
- Tested in beam experiments with different detector orientation

---
Test station at GSI
MBS, Nyx
Signal
generator
(CAEN DT5800D)
Amplifier

---
Generated amplifier input signals

---
Amplifier shaping time: 1.4 and 0.4 μs
4.3° recoil
73.2° recoil

---
Results: energy vs. Vin (short signal)
1 AU ≈ 27 keV

---
Results: integral vs. signal width
- Energy must be corrected
- Individual channel calibration required
1 AU ≈ 27 keV

---
Results: FADC trigger thresholds
0.4 μs shaping
1.4 μs shaping
1.4 μs, 60PT, 60GT
0.1° recoil, "2mv" threshold
mV
Count %
0.4 μs, 60PT, 60GT
0.1° recoil, "2mv" threshold
mV
Count %
0.1°
recoil
~60 keV
1.4 μs, 60PT, 60GT
12.5° recoil, "2mv" threshold
mV
Count %
0.4 μs, 60PT, 60GT
12.5° recoil, "2mv" threshold
mV
Count %
tuning in progress
12.5° recoil

---
Shaping time optimization
- time vs. energy resolution
- full integration vs. beam influence minimization
- smaller shaping for beam anode?

---
Fast FADC readout
- 5 FADCs with 1 Gbit/s Ethernet
- 10 Gbit/s PC link
- ~480 MB/s throughput achieved
- 20x faster than current setup
SIS3316 10G Switch Test by SIS GmbH

---
Conclusions
- High time and energy resolution requirements
- Energy must be corrected
- Thresholds may be lowered
- Time resolution studies with generator are in progress
- Algorithm optimization needed for smaller shaping time (noise filters, possibly higher sampling rate?)
- Goal: final front-end electronics recommendation this year

---
Thank you!

---
CAEN DT5800D Digital Detector Emulator
- 2 analog outputs
- 16 bit D/A converter
- 125 Msamples/s
- Constant/Poisson rate
- 4096 points to store waveforms
- White noise, 1/f noise emulation
- Random Walk (baseline drift)
- Interference generation
- USB, Windows control app

---
Moving average window