## Slide 1: Petersburg Nuclear Physics Institute
DATA ACQUISITION
SYSTEM
PRESS experiment

## Slide 2: DAQ Requirements
Detector system
Time Projection Chamber (TPC)
Forward Tracker (FT)
Beam scintillation counters (S1-S3)
Beam position monitor (BPM)
Beam intensity monitor (BIM)
Time parameters
Beam intensity: 2 MHz
Event rate: <= 50 Hz
Trigger source: TPC
User requirements
Data logging
Online data monitoring

## Slide 3: Forward tracker
Cathode strip chambers (MWPC)
8 chambers (4 XY-layers)
240x2.5mm strips in each chamber
Back side strips joined into 12 strips
2016 channels in total

## Slide 4: Forward tracker electronics
DAQ card (ASF48et)
48 independent readout channels
Digital discriminator in each channel
Option to run adjacent channels
12-bit 25MHz pipeline FADC
Common system clock 100MHz
Memory: L1 1k words per channel, L2 16k words per card
No dead time
Multi-Channel FADC
Intermediate Memory
FPGA Logic
Digital
Discriminator
Front-end
2016 channels
DAQ
interface
Preamplifier
Gain: 40mV/fC
Noise: 800 e-

## Slide 5: ASF48et diagram

## Slide 6: ASF48et signal processing (single channel)

## Slide 7: ASF48et signal processing (external trigger)

## Slide 8: ASF48et with preamplifier

## Slide 9: Forward tracker event rate simulation
 | Card/plane |  |  |  |  |  |  | 
Plane | 1 | 2 | 3 | 4 | 5 | Z | Sum | R/O
FT1 | 2,5h/t | 5,6h/t | 20h/t | 5,6h/t | 2,5h/t | 7,6h/t | 43,8h/t | 90h/t 5760w/t
FT2 | 1,7h/t | 4,6h/t | 26h/t | 4,6h/t | 1,7h/t | 7,6h/t | 46.2h/t | 
FT3 | 1,4h/t | 4,4h/t | 31,5h/t | 4,4h/t | 1,4h/t | 8,6h/t | 51,7h/t | 108,3h/t 6912w/t
FT4 | 1,2h/t | 4,6h/t | 36h/t | 4,6h/t | 1,2h/t | 9h/t | 56,6h/t | 
FT5 | 1,1h/t | 4,8h/t | 41h/t | 4,8h/t | 1,1h/t | 10h/t | 62,8h/t | 132,1h/t 8448w/t
FT6 | 1h/t | 5h/t | 46h/t | 5h/t | 1h/t | 11,3h/t | 69,3h/t | 
FT7 | 1h/t | 5,2h/t | 51h/t | 5,2h/t | 1h/t | 13h/t | 76,4h/t | 158,2h/t 10112w/t
FT8 | 1h/t | 5,4h/t | 55h/t | 5,4h/t | 1h/t | 14h/t | 81,8h/t | 
MC simulation
Beam intensity: 2MHz
200 electrons per event (100s)
Recoil energy: 1-10MeV
Average 6 strips (hits) per track
Total rate in forward tracker at 50Hz trigger rate:
490h/t x 50Hz = 24500 hit/sec
With 60 ADC samples per signal (hit) data rate:
24500 hit/sec х 64words/hit = 1568000 words/sec (3.14 Mbyte/sec)
Average hits per trigger (100s)

## Slide 10: Time Projection Chamber
32+1 channels (8 rings)
100s maximum drift time
Complex trigger logic
System trigger generation
Anode pad layout

## Slide 11: TPC electronics
DAQ card (ASF48eP)
12 independent readout channels
Digital discriminator in each channel Single sample or integrated window
System trigger generation logic
12-bit 25MHz pipeline FADC
Common system clock 100MHz
Memory: L1 8k words per channel, L2 32k words per card
DAQ
interface
Multi-Channel FADC
Intermediate Memory
FPGA Logic
Digital
Discriminator
Trigger logic
Front-end
33
channels
Trigger
Data rate (50Hz trigger):
10 Mbyte/s (avg)
40 Mbyte/s (peak)

## Slide 12: ASF48eP diagram

## Slide 13: ASF48eP signal processing (single channel)

## Slide 14: ASF48eP signal processing (integration window)

## Slide 15: Beam counters electronics
Intermediate Memory
FPGA Logic
Beam Monitor
DAQ
interface
S1
S2
S3
DAQ card (ASF48eP)
800MHz sampling clock (1.25ns resolution)
Common system clock 100MHz
Memory: L1 64 words per channel, L2 8k words per card (1000s at 2MHz beam intensity)
Data rate (2MHz beam): 0.1Mbyte/s per counter

## Slide 16: The whole DAQ electronics layout

## Slide 17: DAQ data flow layout

## Slide 18: DAQ hardware status
Hardware | Design | Production | Firmware
Forward tracker preamplifier | ✓ | in progress | 
Forward tracker digitizer (ASF48et) | ✓ | ✓ | ✓
TPC preamplifier | ? | ? | 
TPC digitizer (ASF48eP) | ✓ | ✓ | in progress
Beam monitor | ✓ | in progress | in progress
Beam position monitor preamplifier | ✓ | in progress | 
Beam position monitor digitizer | ✓ | ✓ | in progress
Beam intensity monitor preamplifier | ✓ | ✓ | 
Beam intensity monitor digitizer | ✓ | ✓ | ✓

## Slide 19: Data acquisition software
ASF48 test software
Full scale DAQ software based on MIDAS (Maximum Integrated Data Acquisition System) http://midas.psi.ch
  Flexible distributed DAQ system
  Web interface for run control and monitoring
  Data transfer / logging capability
  Online data monitoring
  Online database
  Message logging
  Alarms

## Slide 20: ASF48 test software

## Slide 21: Data acquisition software

## Slide 22: FT CSC prototype
Both parallel cathodes
Cosmic tests
Single ASF48et card:
0..23 channels – top
24..47 channels - bottom

## Slide 23: Signal processing

## Slide 24: Cosmic data results
Spatial resolution: 70-80um

## Slide 25: Cosmic data results. Amplitude spectra

## Slide 26: DAQ software status
Software | Status
ASF48 test software | ✓
MIDAS frontend (FT) | in progress
MIDAS frontend (TPC) | in progress
FT signal processing | ✓
FT clipped signal reconstruction | in progress
MIDAS online analyzer | in progress
MIDAS export analyzer | ✓

## Slide 27: DAQ status
Software | Status
ASF48 test software | ✓
MIDAS frontend (FT) | in progress
MIDAS frontend (TPC) | in progress
FT signal processing | ✓
FT clipped signal reconstruction | in progress
MIDAS online analyzer | in progress
MIDAS export analyzer | ✓
Hardware | 
Digitizers for the TPC, FT, Beam detectors | ✓
Beam monitor | in progress
Preamplifiers for the FT, Beam detectors | production
Preamplifiers for the TPC | ?

## Slide 28
Thank you!