## Slide 1: Monte-Carlo studies for the ep-elastic scattering
Aleksei Dziuba \ NRC “Kurchatov institute” - PNPI
31st of March 2021

## Slide 2: Outline
Simulation software strategy
  Goal \ Simulation chain \ Manpower
Current status
What’s new?
  ESEPP generator config https://github.com/nuramatov/esepp/
  Beam smearing at the exit window (already mentioned by Peter Kravtsov)
  Electronic signal https://github.com/aleksha/electronic-signal
  Electronic noise https://github.com/aleksha/electronic-noise
  Drift velocity experiment
  Drift in electric field https://github.com/aleksha/pres-electric-field
  Z-position measurement (angular dependence, power of MVA methods)
  Recoil ranges for calibration

## Slide 3: Run / detector conditions for MC
Beam model
  Time distribution for incoming electrons; mean beam frequency – fb;
  2D beam spatial distribution – Gausx(μbx,σbx)×Gausx(μby,σby) ? Any beam halo?
  Beam direction distribution – Gausp(μpθ,σpθ)×Uniform pφ(-π,π) ?
Geant-4 (detector model) provides ionization
TPC time resolution model
  Drift velocities – Wd1, Wd2; Recombination(rhit, fb); (x,y)-smearing(rhit, fb)
  Accepting due to not clean gas.
  Signal formation (during grid-anode drift)
  TDC parameters:
    Nch, Δtch;  ti – TDC channel
    Energy to TDC response – CTDC;
    Noise spectrum
  Time-pulse function – δDirac(ti)  Some distribution(t,ti,Tj)
These conditions must be included into Monte-Carlo to have is as closer to the data as possible to mimic operation conditions as a function of (beam)time
Goal: MC can be analyzed as DATA

## Slide 4: Software status
All important parts were investigated
New studies (done in 2020-03 – 2021-03) will be presented in the main part of the talk
Software chain of isolated tools, but not a one program 
Manpower:
  Prof. Vorobyev (ideas, coordination, review)
  Aleksei Dziuba (with a large input of ideas and settings from PNPI teams)
  Arsen Nuramatov (bachelor-year student of SPbSU)

## Slide 5: Generators

## Slide 6: Event generators
ESEPP https://github.com/gramolin/esepp to account radiative corrections
We updated a software stack (conda) and now there is a way not to build it with a dependencies-hell (use pres-mc)
A nice config-file (not interactive)
  https://github.com/nuramatov/esepp/
“Handmade” Δ production generation for inelastic (there are more realistic approximation in PRad paper)
There will be no loss in central (not sensitive) part of CSC
Correlation between Tp and electron and proton angle is powerful tool to reject inelastic background
NEW

## Slide 7: Beam smearing

## Slide 8: Beam smearing by main detector
Y
Z
Mylar, 20 μm
Sci + W wire?
H2, 20 atm
Mylar, 50 μm
Ar + CH4 20 atm
CSC
400 mm
TPC volume
Sci, 10 mm
Count electrons
Ionization chamber (for total beam current control)
Beam position chambers (for feedback to MAMI)
CSC = Cathode Strip Chamber
For scattered electrons
Be window
Ti
Be (?) windows
720 MeV electron beam
720 MeV electron beam
Calibration purposes
Cathode
Grid
Anode

## Slide 9: Beam smearing at the exit window
20 bars
5 bars

## Slide 10: Induced current (during grid-anode drift)

## Slide 11
Problem: signal is created during grid-anode drift. Additional smearing to a signal shaping
This method is suggested by Alexander Dobrovolsky (PNPI)
  Добровольский Александр Владимирович
  dobrovolsky_av@pnpi.nrcki.ru
Based on Grinberg’s textbook
Simulation tool uses CERN.ROOT framework
  https://root.cern.ch/
Anode current calculation
Electronic signal tool: https://github.com/aleksha/electronic-signal

## Slide 12: Charge between two infinite planes
pp.113
From potential one can go to the induced charge using Gauss theorem
L – distance between planes
r – radial distance from a charge
h – distance between plane and charge
q – electron charge (q=-1)

## Slide 13: The method in a nutshell
Create a map of induced charge on rings with fixed width for an electron which is moving perpendicular to anode at r=0.
Calculate induced charge and induced current (as a derivative of the induced charge) with defined anode structure for an electron in point (x,y) using an overlap of the map and anodes.
Find which of anode is fired, using the largest integral of current.
Rescale currents for each of anodes with a common factor, which is evaluated to set the current integral for the fired anode to unity.

## Slide 14: Induced charge and current for x=12mm, y=18mm
Central pad (r=10 mm)
1st ring (width 40 mm)
2nd ring (width 40 mm)
Note that it isn’t zero!
Numerical errors (too close r order of h)
Example of a tool result
Agreement with the expected behavior
Need to speed it up
As well as integration into a software chain
Electronic signal tool: https://github.com/aleksha/electronic-signal

## Slide 15: Modification of the response functions
Signal appears when electron reach anode
Current during Grid-Anode drift
Current is assumed to be constant, while electron drifting between Grid and Anode
Zero time – time, when electron is on the grid
L GridAnode = 10 mm; W2 = 7,5 mm/μs
Many thanks to Alexander Dobrovolsky, who pointed me on the problem!

## Slide 16: Drift velocity measurements

## Slide 17: Calibration of drift velocities
Triggering from incoming beam electron. Time between beam and TPC response is known (with a precision discussed today).
MAMI has excellent beam. The ionization-anode distance is known with 0,1 mm precision.
titanium

## Slide 18: All pads
1
3
2
5
4
6
7
9
8
10
15
14
12
13
16
11
Central pad is a circle with 1 cm radius
Others are half-rings with 4 cm width
Numbering as on sketch
X
Beam
0
1st anode
16th anode

## Slide 19: Longitudinal diffusion of electrons
σZ = 0,008 × √LTrackGrid
[σZ] = [LTrackGrid] = cm
Parametrization by German Korolev (private communication via Alexey Vorobyev)
Smear Z-position for each ionization electron by a Gaussian function with σZ.
LTrackGrid = 25 cm
10000 of beam electrons (a part of spectrum around the peak is presented)
Peak maximum as a time-point estimator
Noise OFF
With longitudinal diffusion
No diffusion

## Slide 20
A scatter around a smooth curve indicates the accuracy of the estimate!
A bias for the maximum position estimator is on nanosecond-scale. Good enough!
With diffusion
Without diffusion

## Slide 21: Increase diffusion parameter by factor 4
8-9 ns shift at 250 mm

## Slide 22: Electronic noise simulation + influence on a drift velocity measurement

## Slide 23: Further studies of noise + simulation
See more details https://github.com/aleksha/G4-Models/tree/master/Data/Noise
Noise in data (baseline corrected)
Generated noise
Obtain distribution for real and imaginary part of frequency spectra using Fourier transformation;
Fit these distributions using two gaussian hypotheses;
Generate random spectrum out of these distributions;
Use inverse Fourier transformation to obtain spectrum of generated events.
Now it’s fast! (factor 1000 wrt 1st version)
Thanks to Arsen Nuramatov

## Slide 24: Maximum (peak position) shift due to noise
Peak is placed to the random location of cumulative noise spectrum
Shift of maximum for signal + noise (blue) wrt. pure signal (green)
Some fit examples
Noise ON

## Slide 25: Distribution for shifts for 100k events
100 random places for signal peak at the noise spectrum. Signal shape at the peak region and cumulative noise spectra are same, but position is different!
RMS for maximum with peak position fitting procedure 6,1 ns

## Slide 26: Electric field uniformity

## Slide 27: Electric field uniformity + drift of electrons
Electric field calculations are done by Kuzma Ivshin using COMSOL package.
Electron is drifted in the electric field. Its track is a series of the steps, defined by a step parameter. A typical step size (of 0.1 mm) is order of magnitude less than a spatial grid size for the electric field (5 mm).
A direction for the step is chosen according to a unit vector parallel to an electric field direction.
Electric field components in a beginning of a step are inferred by an interpolation procedure (tri-linear interpolation).
Tool to calculate shifts https://github.com/aleksha/pres-electric-field

## Slide 28: Electric field uniformity + drift of electrons
No radial shift if Ex and Ey are set to zero
Some radial shift for the full field map
The direction of this is to the center of TPC!
There is strong Rin and Zin dependence
Tool https://github.com/aleksha/pres-electric-field
Further development is needed (interpolation-based shift procedure)

## Slide 29: Issue with a Z-positioning

## Slide 30: A problem of Z-positioning
PRES experiment requires a Q2 scale calibration, which will be done using a measurement of an angle of the scattered electron.
Measurement will be done with a first layer of multiwire and Z coordinate of a scattering point measured by a TPC (X and Y assumed to be zero due to the perfect MAMI beam).
Z is measured on the 1st anode ring by finding of a stable timestamp point from the FADC signal. Central pad has twice worser resolution due it’s small size (relatively higher electronic noise) and due to the beam noise.
Signal shapes depends on a scattering angle of the proton (T fixed)

## Slide 31: Time point measurement (~40 ns resolution)
Start point, measured using front intersection with a baseline
Time when e- reach grid
Time e- reach anode
1333 ns
Maximum distribution (pol2-fit)
T = 5 MeV
Noise ON
1st ring

## Slide 32: The problem
T = 5 MeV
Angle wrt. Y-axis
Noise OFF
1st ring
Cumulative spectra
0 deg
wrt. Y
5 deg
RMS = 40 ns
1st ring
600 ns
Strong dependence
Peak position
Uncertainty for a single event

## Slide 33: Pure electron signal (a cross check)
Idea by Alexander Inglessi
Electrons arrive at grid
Induced current
0 deg.
0 deg.
w/o diffusion
with diffusion
5 deg.
5 deg.
2,5 deg.
2,5 deg.
5 deg  Signal projection 0,087*40mm = 3,48 mm  Signal length 870 ns
Note, that y-scale are different, but integrals are the same!

## Slide 34: Pure electron signal (a cross check)
Idea by Alexander Inglessi
Electrons arrive at grid
Drift + Electronic response function
0 deg.
0 deg.
5 deg.
5 deg.
2,5 deg.
2,5 deg.
5 deg  Signal projection 0,087*40mm = 3,48 mm  Signal length 870 ns

## Slide 35: Correction by TPC information
Recoil angle can be measured by TPC
Correction on a measured angle
0,3-0,4 mm resolution of simple algorithm, when offset is estimated from the measured angle
Multivariate analysis (MLP) can make 0,2 mm resolution accessible (next slides)
mean : 5.31285 rms : 0.999505
Angle measiured by 1st and 2nd rings
MC truth 5 deg.

## Slide 36: MVA regression as an estimator
Uniform pdf
  ZTRUE = (190, 210) mm
  ThetaTRUE = (0, 6) deg
  TTRUE = (4,5, 5,5) MeV
Standard ROOT::TMVA example
  Multi Layer Perceptron (MLP)
  Boosted decision tree (BDT)
  Linear discriminant analysis (LD)
Z or polar angle as target variable
800 events for training / 150 for test
To be compared with 0,3-0,4 mm resolution o simple algorithm, when offset is estimated from the measured angle

## Slide 37: First MVA results (Z as a target)
=====================================================
MVA Method: <Bias> <Bias_T> RMS RMS_T
=====================================================
9 variables (start, peak, end) from central anode and first two rings
-----------------------------------------------------
MLP : -0.0246 -0.0299 0.166 0.140
LD : -0.0310 -0.0366 0.174 0.146
BDT : -0.0177 -0.0126 0.229 0.191
Indicated by "_T" are the corresponding "truncated" quantities obtained when removing events deviating more than 2sigma from average.
Optimization is required
To be compared with 0,3-0,4 mm resolution of simple algorithm, when offset is estimated from the measured angle

## Slide 38: First MVA results (angle as a target)
=====================================================
MVA Method: <Bias> <Bias_T> RMS RMS_T
=====================================================
9 variables (start, peak, end) from central anode and first two rings
-----------------------------------------------------
MLP : -0.00304 0.0196 0.538 0.435
LD : 0.0274 0.0215 0.539 0.451
To be compared with ~1,0 deg resolution (see slide 4)
Optimization is required
Conclusion: we have to use full power of MVA in our analysis

## Slide 39: Real life (well it’s ESEPP)
Recoil angle, deg
Electron angle, deg
5 MeV
10 MeV
2 MeV
Estimates at the previous slide is done for this point
ESEPP configuration:
Photon cut 0,5 MeV
Point-like proton
E=720 MeV
Lepton cut 5 deg.
Maximon & Tjon
Full other rad.calc
https://github.com/gramolin/esepp

## Slide 40: ESEPP
Recoil angle, deg
Recoil energy, MeV
Three problems in the middle:
Radiative processes (aka corrections) can create recoils with higher energy which stop between anodes
Same but via in-elastic processes (with pions)
A certain signal detection limit can produce bias
Quite close to linear
One should not expect large quadratic effects in Z-scale calibration

## Slide 41: Range measurement

## Slide 42: Energy by stop between anodes
Between 2 and 3
Between 3 and 4
Between 4 and 5
Between 2 and 3
Gen.Cut on TR
Gen.Cut on TR
Between 2 and 3
7000ev

## Slide 43: +/- 100 keV range, 7000 events
True TR
Reconstructed TR

## Slide 44: Stopped on edge between 2nd and 3rd rings
True TR
Reconstructed TR
True = 4.9797 +- 0.0008 MeV
Rec. = 4.9753 +- 0.0010 MeV
True – Rec. = -4.4 keV (-4.3σ)
Asymmetry
Find zero crossing

## Slide 45: Same energy, same angles, but bias due to Zrec
Z
0 mm
400 mm
TPC
MWPC
700 mm
P (far)
P (close)
e
e
Identical events with θ=5 deg. (87 mrad)  Time bias 600 ns
 +2,4 mm to a true position wrt. anode
Bias in reconstructed θ  Far: 0,3 mrad (resolution 0,04 mrad)
 Close: 0,7 mrad (resolution 0,10 mrad)
Difference order of 0,4 mrad  to measure in MC
l

## Slide 46: Z-dependent bias in reconstructed angle
Close to anode (Far)
Close to cathode (Close)
Center of TPC
Mean +/- Error of Mean
Mean value of the bias of reconstructed θ (TPC-MWPC based) with respect to a true one depends on Z
Bias correction  put peak into ZTRUE
Still some bias, which is higher for higher Z, as expected
Why?!! Misalignment?

## Slide 47: Yes! This was a mistype in code  misalignment
Everything fine but requires MC calibration constant!

## Slide 48: Find tune parameter from best fit by constant
For each shift calculate χ2 with respect to a constant hypothesis
7000 events,
Electron scattering angle is calculated in 18 bins along the Z axis
Δχ2=1 to estimate confidence interval
Uncertainty of 0,04 mrad, which is 1,8*10–4 relative precision
±σ
±σ
Δχ2=1

## Slide 49: Absolute measurement of angle
Z
0 mm
400 mm
TPC
700 mm
p (far)
p (close)
e
e
Δl
ΔZ
θ = atan( Δl/ ΔZ )
Identical TR events using range measurement ( T23+/- 50 keV)
Take ΔZ to be some large value (I use 180 mm)
θ = atan( Δl/ ΔZ )
Idea of Nikolay Voropaev: Slice on Z and fit Z-l curve to obtain angle
Radiation tail produce problems
MWPC

## Slide 50: Median as robust estimator for an angle
Median for 2body sample
Median for ESEPP sample
ESEPP sample
2body sample
Mean for ESEPP sample
Effect of the Ephoton cut-off
Mode ESEPP sample
(window dependent)

## Slide 51: Absolute measurement of angle
σ Median = 3.52 + 0.013×ΔZ
(from pseudoexperiments)
An angle obtained from the slope
θmed.est = 135.112 ± 0.021 mrad
was compared with a median true value of scattering angle
θtrue = 135.147 mrad.
The relative precision for θmed.est is 1.5×10–4.
A difference between estimated and true value of the median scattering angle of 0.035 mrad is accounted as a bias introduced by the method.
Expressed in the standard deviation of the procedure it states that the reconstructed angle in in 1.5σ agreement with the true one.
Median of hit position at 1st layer of MWPC, mm
Distance between hit and MWPC position, mm

## Slide 52: Conclusions
All the aspects are considered
Many improvements
  Signal treatment
  Noise tool
  Drift velocity studies
  Z-position issue
We are trying to create a single project \ applanation for MC
Certain lack of manpower